## Slide 1: RFID for Breath Monitoring
Jiaqi Wu, Ranxuan Zhang, Birtukan Fozzati

## Slide 2: INTRODUCTION: BACKGROUND
Respiration and heart rates are vital health indicators in healthcare
Traditional methods :intrusive, less practical, expensive
Example: RMMI
Figure1.RMMI at Sahlgrenska
Bulky
Expensive
Patient Discomfort
Requires Regular Maintenance
Limited portability
Sensitive to external interference

## Slide 3: INTRODUCTION: BACKGROUND
Wireless Methods
Pros: Non-intrusive, user-friendly
Challenges:
  Limited range
  Signal interference
  Difficulty recognizing multiple users at once
RFID Technology
Pros:
  Unique user identification and differentiation
  Cost-effective

## Slide 4: INTRODUCTION: PURPOSE
Objective:
Implement an RFID-based approach for traking respiratory motion using passive RFID tags
Technlogy: wireless tags and reader
Components:
RFID Reader : Sends signals,receives data,detects position
RFID Tag: Small device( active/passive) that stores and shares data with reader

## Slide 5
Methods
System Setup
• Fix antenna
• Power the reader and Connect to the antenna and computer
• Prepare tag
• Application for data report
ItemTest, Octane SDK
• Ground truth
Test
OpenSignals
Normal breathing
Deep breathing
Hybrid breathing

## Slide 6: Method
Data preprocess
• phase ambiguity
• phase transition​
Respiratory rate extraction:
DC (zero frequency) component removal
Butter-​worth bandpass filtering
Fast Fourier Transform (FFT)

## Slide 7: Results
Resulted phase: 7 peaks
Resulted phase: 7 peaks
Reference value from Opensignal: 7 peaks for 30s
Frequency: 0.23
Frequency: 0.23
*RIP sensor only detects the ground truth on the abedomen

## Slide 8: Results
Change from normal breath to deep breath
Hybrid breathing

## Slide 9: Discussion
RFID technology can effectively track respiratory movements from different body part
Signal amplitudes differ across body sides due to natural asymmetry.
Tags on cloth (tight or loose)
Sitting or lying
Initialization

## Slide 10: Future work
Hardware:
  Develop a better way to attach the tag to the body
  Optimize the placement and setup of the device
  Use a dummy model to obtain more accurate ground truth values
Software:
  Validate and refine the phase processing algorithm
  Implement real-time signal display for RFID data.
  Package and integrate the existing system to meet clinical requirements.
Data:
  Test on more people.
  Different distance between antenna and tags

## Slide 11
Conclusion
Successfully measured basic respiratory rate for different body part, capturing phase and distance.
The data quality from different part, especially the chest part, seems to highly depend on the breathing method
(stomach/chest).
Challenges
Chest Tags: Limited performance; improved with varied breathing techniques
Clothing Fit: Loose clothing affected readings ;lying down helped improve accuracy
Data Stability: Results were inconsistent; may need more preprocessing
Tag and Antenna Position: Requires optimization for improved reliability

## Slide 12
Thank you!